## Slide 1: The Physical Internet

## Slide 2: The Internet
What does it look like?
A network of networks
https://xkcd.com/

## Slide 3: You (The End User)
How do you connect to the Internet?
Wireless Router
https://www.amazon.com/Linksys-WRT54G-Wireless-G-Router/dp/B00007KDVI
Wireless Access Point (WAP)
http://us.dlink.com/product-category/business-solutions/wireless/software-managed-access-points/
Ethernet
https://www.digitaltrends.com/computing/differences-between-ethernet-cables/

## Slide 4: You
However you connect your machine to your network
  you are connected to everyone else on that network
  We often call this a Local Area Network (LAN)
  Great for gaming will almost no lag
To connect to the Internet
  Connect a router in the network to a larger network
  Most commonly an Internet Service Provider (ISP) network through a modem
Router
  Multiple devices can use the same connection
Modem
  Decodes signals from ISP
https://kb.netgear.com/30985/How-to-manually-configure-a-PnP-connection-with-Etisalat-on-your-NETGEAR-Nighthawk-router

## Slide 5: ISP Networks
Connect customers to the Internet
Maintain city and regional networks
Addresses the last mile problem
  Part of a network connecting to individuals
  Requires onsite technicians for each connection
http://oldforum.paradoxplaza.com/forum/showthread.php?837998-Underground-power-lines-and-capacity/page2
https://bijanghayyoomi.files.wordpress.com/2010/08/picture20.jpg

## Slide 6: Tier 1 Networks
A network that is connected to all other networks on the Internet without paying another network provider for access
Maintain networks at the global scale
ISP’s pay for tier 1 access just like we pay ISPs
Tier one networks form the backbone of the Internet
Some tier 1 companies also offer ISP services to individuals in certain regions
Often peer with each other allowing them to use each other’s networks, thus increasing the overall speed and reliability of the Internet

## Slide 7: Tier 1 Networks
AT&T
CenturyLink
Global Telcon & Communications
Level 3 Communications
NTT Communications
Verizon Enterprise Solutions
Zayo Group
(https://en.wikipedia.org/wiki/Tier_1_network for more)
http://www.vootwerk.com/network.html

## Slide 8: Internet Exchanges (IX)
Tier 1 networks must connect to ISP networks and other Tier 1 networks
These connections are made in Internet Exchanges
60 Hudson Street (pictured) houses one such IX in Manhattan
IXs maintain many connections and require reliable power and various backups
https://en.wikipedia.org/wiki/60_Hudson_Street
https://www.wired.com/2015/11/peter-garritano-where-the-internet-lives/

## Slide 9: Connecting Continents
We routinely use the Internet to connect to people from around the world
This means our data is being routed across oceans to other continents
Discussion: How does this work?

## Slide 11
https://arstechnica.com/information-technology/2016/05/how-the-internet-works-submarine-cables-data-centres-last-mile/

## Slide 12: First Submarine Cable
Spanned the Atlantic Ocean and Connected
  Ireland
  Newfoundland
Laid in 1858
Used to send telegraphs

## Slide 14: Content Delivery Network (CDN)
Everything we want to use needs to be connected to the Internet through networks
ISPs and Tier 1 networks route data through the Internet
CDNs connect the content we want to consume to the rest of the Internet
Large CDNs contain multiple sites in different parts of the country, or world
  Increased speed
  Don’t always to send a request to the company headquarters

## Slide 15: CDN - Power and Storage
Popular CDNs have significant amounts of data to process
CDN receives many requests for data (Websites, snaps, streams, messages, etc)
Server
  A computer designed to be housed in a server rack
  Not made for personal use
  Usually contains hardware specific to its role in the network
A CDN handling millions of users (ex. Twitter, Google, Amazon) needs many, many servers to maintain speed for every user
CDNs for popular services also store massive amounts of data
  How much storage does Twitter need in order to store every tweet ever?
  How about YouTube storing every video ever uploaded to the site?
Use server farms to store all this processing power and storage

## Slide 16
http://americanbuildersquarterly.com/2015/yahoo/

## Slide 17
http://imgur.com/gallery/7NPNf

## Slide 18: CDN - Bandwidth
Pay the ISP’s and Tier 1 companies to deliver their content
Similar to an end user, though bandwidth requirements can be huge
  How much bandwidth does Google need in order to keep YouTube running?
  How much bandwidth does Netflix need to stream to all of its customers?
Downsides
  This can be extremely expensive!
  Leaves CDN helpless in the case of network outages
Some companies lay their own cable to create CDN backbones
  Increase bandwidth
  Become more independent
  Reduce long-term cost
Other networks deliver data to the CDN backbone. CDN delivers it to its destination

## Slide 19
https://www.blog.google/topics/google-cloud/google-invests-indigo-undersea-cable-improve-cloud-infrastructure-southeast-asia/

## Slide 20: TopHat

## Slide 21: Net Neutrality
With Net Neutrality
  ISPs must treat all data transfer over its network with equal priority
Without Net Neutrality
  ISPs can prioritize certain data transfers however they choose
  Can slow down requests made for certain CDNs
  Can create “fast lanes” for CDNs at their will, or for profit
We currently have had net neutrality in the US
  ISPs are fought relentlessly fighting to change this
  They lobby lawmakers with our money
Some countries do not have net neutrality today
  The Chinese government control much of what their citizens can access on the Internet
  The Russian government requires ISPs to block certain sites or face fines
  Australia has no laws in place to protect Net Neutrality and ISPs are free to do what they wish

## Slide 22: Net Neutrality
The network (business) side
  We’ve spent billions of dollars laying cable with the intent to make a profit
  We should be able to earn that profit however we see fit
The user (human) side
  The Internet has revolutionized the world
  Do we risk slowing down civilization just to please the shareholders of a few companies?
  Do we destroy the profits for countless other companies in the process?
Discussion: What do you think about Net Neutrality?

## Slide 23: Discussion
On TopHat!

## Slide 24: Spread Networks
What if ISP’s and Tier 1’s are not fast enough
http://spreadnetworks.com/network-map/

## Slide 25: Spread Networks
Built a tunnel carrying fiber optic cable connecting Chicago and NYC
Cost hundreds of millions of dollars
Round trip time between the two cities
  13ms (0.013 seconds)
Round trip time for a typical customers of ISP’s?
  16ms (0.016 seconds)!
Read more: https://www.nytimes.com/2014/04/14/opinion/krugman-three-expensive-milliseconds.html

## Slide 26: Spread Networks
Why fund a 9 figure project to save 3ms? Why these cities?
  High volume trading
NYC
  Home of the NASDAQ
  Trade stocks
Chicago
  Home of the Chicago Mercantile Exchange
  Trade futures and options (Derivatives of stocks)
Arbitrage
  Step 1: Detect a price discrepancy between a future or derivative and its underlying stock
  Step 2: ??? (Probably a degree in finance)
  Step 3: Profit!
Only one catch. You have to be first.
  If 3ms is enough time to place your trade before anyone else, that’s YOUR profit!

## Slide 27: Internet Protocol

## Slide 28: Internet Protocol (IP)
We saw that the Internet is a network of networks connected by cables
Now, how do these networks and devices communicate with each other?
  Don’t want to broadcast our data to everyone on the Internet
To connect to a specific server on the Internet we use the Internet Protocol
  Official standard for IPv4: https://tools.ietf.org/html/rfc760
IP address
  Every device connected to the Internet has an IP address
  That device’s “location” on the Internet
  To connect to specific device, send data to its IP address
  Similar to send mail to a street address in the physical world

## Slide 29: Internet Protocol
Data is sent in packets
Each packet contains a header and a payload
Header
  Contains metadata about the packet
  Most importantly, contains the source and destination IP addresses
Payload
  The data to be send to the destination device
  IP has no concern about the content of the payload
  IP is only concerns about delivering the payload to its destination
  Payload often/always follows additional protocols agreed upon by the source and destination
    Ex: TCP, UDP, HTTP
  Payload is often encrypted

## Slide 30: IP
Address of a machine on the Internet
  Ex: 172.217.12.211
Routers read the address and send it to the next step
Often read a prefix
IPs with a common prefix are related
Two parts: Network, host
Organizations will receive a prefix and own all IP’s that start with that prefix
  One of Google’s ranges: 172.217.0.0-172.217.255.255
    Network prefix: 172.217.x.x

## Slide 31: IP
IPv4 (8.8.4.4)
  Consists of 4 numbers ranging from 0 to 255
  How many total addresses?
    4 numbers, 8 bits each, 32 total bits, 2^32 total addresses
    4,294,967,296
  A lot, but not enough
IPv6 (2001:4860:4860:0000:0000:0000:0000:8844)
  128 bit addresses
  2^128 total addresses
    340,282,366,920,938,463,463,374,607,431,768,211,456
  That should be enough
  Used in conjunction with IPv4
  Routers must be able to route both versions

## Slide 32
From the IPv4 official standard: https://tools.ietf.org/html/rfc791

## Slide 33: Domain Name Service (DNS)
We don’t want to remember IP address for all our favorite sites
With DNS, we don’t have to
DNS
  Remember a Domain Name instead of an IP address
  Domain Name: google.com
  When you click a link, first a DNS request is made to get the IP address for that Domain Name
  Then the IP address is used to make your request
Can access sites directly by IP
  http://172.217.6.228/
Not all sites allow direct IP access
  http://104.16.40.2/

## Slide 34: Routing Through the Internet
ISP and Tier 1 networks contain many routers to direct Internet traffic
  These routers are made for speed!
  To maximize speed, they are simple
  The complexity of the Internet is in the users and CDNs
Router reads the destination IP address of a packet and sends it to the next router
  Only knows the next step
  No one needs to map the entire Internet
  Networks change
  Routing tables can be updated
https://superuser.com/questions/959242/how-is-next-hop-defined-in-routing-table

## Slide 35: Transmission Control Protocol (TCP)
The Internet is unreliable
  Router sends a packet to its next step, then forgets about it
  May have sent packets to a failed router
  Cables may be cut
  Regions can have power outages
  Router never gets confirmation of delivery even if the packet made it to its destination
Internet users and CDNs are responsible for reliability
How?
  Timeout
  TCP

## Slide 36: TCP: Making a Connection
3-way handshake to confirm a connection
SYN
  Client sends a packet with a random number to the server
SYN-ACK
  Server acknowledges that it received the client’s SYN by returning the random number+1
  Also send another random number
ACK
  Client returns the server's random number plus 1
After all three steps, boths side have verified the connection
https://lwn.net/Articles/508865/

## Slide 37: TCP: Transmitting Data
Data is often too large for a single packet
Divide data into smaller packets
Receiver reassembles the packets on the other side of the Internet
Once a connection is established, send all the packets
Packets can arrive out of order
  Each packet contains a sequence number for reordering
  If a sequence number is missing, request a resend
Many streams simultaneously
  TCP uses port numbers
  Port number routes communication at the machine level
  Different programs communicate with different ports
  Allows multiple programs to all use the Internet
  Ex: Web browsers use ports 80 and 443

## Slide 38: Live Demos
How long does it take to load a website? (Browser console)
What’s the path of a packet? (Traceroute)

## Slide 39: A Thought on Security and Privacy
How to secure your data and protect your privacy?
  Encryption!
  More later
No matter how you encrypt your data, your ISP and Tier 1 networks must always know 2 things:
  Source IP Address
  Destination IP Address
Therefore: They HAVE to know what servers you’re connecting to, even if they don’t know what you are saying

## Slide 40: A Thought on Security and Privacy (VPN)
Virtual Private Network (VPN)
  Originally used to connect to a network remotely (ex. UB’s AnyConnect)
  Commonly used to “Bounce” web requests off the remote server
  The VPN can send requests on your behalf and return the response to you
Can increase privacy
Can effectively scramble communication if many users go through the same VPN
Does not ensure privacy
  Must trust the VPN provider
  Routers still know you’re connecting to a VPN
  CDNs can block traffic from known VPN IP addresses
    Important: This is not a violation of net neutrality since CDNs are not ISPs!

## Slide 41: Course Evaluations

## Slide 42: Please Give Us Your Feedback
For your extra 3 points, both need to be 80% or higher.
Check your email for the link to CSE 199 survey.
Both close on 12/9 (this Sunday).
The winning section for extra 2 points is A at this point.
 | University Course Evaluation | CSE 199 Survey
Section A | 37% | 30%
Section B | 50% | 15%
Section C | 46% | 13%
Section D | 36% | 13%
Section E | 43% | 13%
Section F | 51% | 13%

## Slide 43: HTTP

## Slide 44: How did we get here?
The physical Internet
  The Internet is a network of networks
  Physically connected by cables and routers
Internet Protocol (IP)
  How routers move data through the Internet
  Best effort basis
Transport Control Protocol (TCP)
  Transport information reliably through an unreliable network
  Used by the client and server

## Slide 45: Network Stack
Enter HTTP
Packet Structure
IP
TCP
HTTP
Content

## Slide 46: HyperText Transfer Protocol (HTTP)
HTTP is an Application Protocol
  Protocols that are not concerned with the transmission of data
  Standards for what we do with the data
Used to access data, web sites, and web apps
[Almost] Always uses TCP for reliable communication

## Slide 47: HTTP: Client - Server
HTTP add structure to the communication between a client and a server
Request - Response protocol
  Client makes request to server
  Server returns a response
  Ex. Request The latest tweets from a user. Twitter server returns the tweets in its response
Response can require more requests
  Each image on a web site requires another request
  Required libraries need to be downloaded (JQuery, Bootstrap)
Can contain links that make other requests

## Slide 48: HTTP
HTTP is a stateless protocol
  Saves time and memory on the server
  Each request is handled in isolation even if a client just made another request
If state is desired (ex. Login) it must sent the state with each request
  Cookies
  Tokens

## Slide 49: Response codes
200 OK
  Request was handled as expected
301 Moved Permanently
  Redirect to the new location
304 Not Modified
  File in local cache can be used
403 Forbidden
  You don’t have access to the requested page
404 Not Found
  Requested data could not be found
500
  Internal server error

## Slide 50: URL
Structure:
Protocol://server_name/resource
Protocol
  Ex: HTTP
Server name
  Ex: buffalo.edu
Resource
  Ex: home.html

## Slide 51: HTTP Requests
GET Request
Request information from a server
POST Request
Send information to a server (Forms)

## Slide 52: Security
Client downloads the entire code for a site and you run it in your browser
The client has all the code needed to run the site in their browser. Clients can make any changes they want!
JavaScript console. Edit html. Edit requests directly.

## Slide 53: Security
Server must verify every request
Never trust your clients
DRM? Always online replaced older drm. Anything client side will eventually be cracked

## Slide 54: Security and privacy
ISPs, tier 1, local network owners, and everyone in range of your WiFi can read your stuff!

## Slide 55: HTTPS
Encrypted version of HTTP
Privacy
You verify the server’s identity
Server verifies your identity
Signified by a green lock on most browsers

## Slide 56: Who to Trust
Certificate authority. Must trust the CAs. In the end, all security comes down to trusting someone. In this case you trust your browser, the CA, the site you're using.
More likely, you trust that if these large organizations we're doing something wrong that someone else would call them out for you
Even with trust, are they competent?
Remember: others still know who you're talking to, but not what you're saying. They can also know how much you are talking